## Slide 1: Fertilizer Applicator Training
May 9, 2014

## Slide 2: Fertilizer Use Act of 2011
Maryland’s Lawn Fertilizer Law

## Slide 3: Fertilizer that’s good for turf can be bad for the water.

## Slide 4: Fertilizer Risk
Nitrogen & phosphorus are primary parts of fertilizer.
When nitrogen & phosphorus get in the water, they cause excessive algae growth
As the algae die and decompose, they use up the oxygen in the water
This leads to “dead zones” in the Bay
Without oxygen, fish, crabs, and other aquatic creatures die, too.

## Slide 5: Fertilizer Risk cont’d
To comply with the Clean Water Act, Maryland and other nearby states are required to reduce the amount of nitrogen and phosphorus entering the Chesapeake Bay.
The new fertilizer law was designed to keep fertilizer out of the water.

## Slide 6: There are two ways for nutrients to get into the water: leach down through the soil or wash off the surface, either alone or with eroded soil
runoff
Leaching to groundwater

## Slide 7: Certification is Required
To ensure that paid fertilizer applicators apply fertilizer correctly, they must be certified, or work under the direct supervision of someone who is.
A person must pass a test to become a Certified Professional Fertilizer Applicator (CPFA).

## Slide 8: Nutrient Needs of Turf
Grass, like all plants, needs 16 nutrients for growth.
These nutrients come from the air, water, and mostly from the soil.
Fertilizers supplement the nutrients in the soil. The nutrients typically included in fertilizers are:
Nitrogen
Phosphorus
Potassium
These are the nutrients that plants use in the largest amounts.

## Slide 9: A Little Bit About Grass

## Slide 10: Kinds of Grass
There are many kinds of grass that grow in Maryland, but only a few that are suitable for home lawns.
These can be divided into cool season and warm season grasses.

## Slide 11: Kinds of Grass cont’d
Cool season grasses grow best in the early spring and the fall. In the heat of the summer, they grow very slowly and may turn straw-colored.
Warm season grasses grow well in the hot summer, but turn straw-colored after the first frost.

## Slide 12: Fertilize at the Right Time
Grass should be fertilized when it is actively growing so the roots will take up the fertilizer.
This decreases the risk that the fertilizer will leach down through the soil and into the groundwater.
Fertilize warm season grasses after dormancy breaks through the end of August.

## Slide 13: Fertilize at the Right Time cont’d
Fertilization of cool season grasses is a little more complicated.
Fertilizer applied in the spring causes rapid top-growth.
Fertilizer applied in the fall grows and strengthens the roots.
Most of the total annual amount of fertilizer should be applied to cool season grass in the fall.

## Slide 14: Soil Testing

## Slide 15: Why Soil Test?
It is the only way to accurately determine nutrient needs of turf.
To determine pH (or acidity) of the soil.
It helps to diagnose problems.
It is required in order to apply phosphorus.
A soil test is valid for three years

## Slide 16: pH
Is a measure of the level of acidity in soil
Scale of 1to 14
If pH is too high, or too low, nutrients in the soil will not be available for uptake by the plant.
Low pH is corrected with lime, high pH is corrected by sulfur.
Ideal pH for turf is slightly acidic, or less than 7.

## Slide 17: Proper Soil Testing
The area should:
Have similar soil types and fertility levels
Have been managed the same in the past
Be managed the same in the future
A Management Unit is the land area that can be covered by a single soil sample.

## Slide 18: Proper Soil Testing cont’d
Take a separate soil sample for:
Unusual or different soil conditions
  Wetter or dryer
  Imported fill, topsoil, or organic matter
Shade vs. sun
Poor plant performance
These should be a different management unit

## Slide 19: Proper Soil Testing cont’d 2
The accuracy of a soil test depends largely on the quality of the soil sample submitted.
Walk the grounds
Interview the homeowner
  Ask about problems
  Learn about any past treatments and results

## Slide 20: Soil Sampling
Sample to depth of 3-4 inches for turf
Use a soil probe or spade
Collect 12-15 subsamples from each management unit, covering the area in a zigzag or W shaped pattern
Avoid areas that are obviously different, such as a patch of dead grass or a low spot
Remove surface litter, stones, roots and debris

## Slide 21: Soil Sampling cont’d
Mix together in a plastic bucket.
Mix the subsamples thoroughly, because only a very small amount of the soil will actually be tested.
Air dry the samples, do not heat in an oven.
Send about 1 cup of soil to the lab.
Use an approved lab listed in Appendix C of Maryland’s Professional Lawn Care Manual.

## Slide 22: Measuring Area

## Slide 23: Measuring Area
To determine how much fertilizer is needed, you must know the size of the property.
Applying the correct amount of fertilizer helps the grass to grow without leaving excess fertilizer to runoff or leach.

## Slide 24: Measuring Area cont’d
The CPFA or an estimator will normally measure the property and determine how much fertilizer is needed.
Be alert for changes that might affect how much fertilizer is needed.
Has the homeowner reduced the turf area by adding a garden? Be sure to notify your supervisor.

## Slide 25: Measuring Area cont’d 2
There are several computer programs that enable you to measure an area remotely
Sometimes, a good old-fashioned measuring wheel is used.
Measure the entire property and subtract the areas that don’t get fertilizer. The remainder is the fertilized area.

## Slide 26: Break oddly shaped properties into simple shapes
House
driveway
garden

## Slide 27: Here’s a Rectangle

## Slide 28: Here’s a Triangle

## Slide 29: Here’s Half of a Circle

## Slide 30: Here’s Rectangle B

## Slide 31: Measuring Area- rectangle
Rectangle Area = Length x Width

## Slide 32: Measuring Area- triangle
Triangle Area = ½ base x height
base
height

## Slide 33: Measuring Area- circle
  Circle area = 3.14 x radius x radius
radius

## Slide 34: Add together the parts to get total area of the property:
Rectangle A
+ Triangle #1
=Area of Property

## Slide 35: Subtract areas not fertilized

## Slide 36: To get the fertilized area:
Rectangle A
+ Triangle
- House (Rectangle B)
- Driveway (1/2 of Circle)
=Area Fertilized

## Slide 37: Equipment Calibration

## Slide 38: Equipment Calibration cont’d
The CPFA is responsible for ensuring that spreaders are properly calibrated.
Most professional-grade products come with suggested spreader settings.
Spreaders must be calibrated to ensure these settings are correct.

## Slide 39: Equipment Calibration continued
The goal of calibration is to determine how much fertilizer is being applied per unit area, or the application rate.
There are two factors that affect the fertilizer application rate, the spreader setting, and the applicator’s walking speed.

## Slide 40: Equipment Calibration- granular fertilizer
Both broadcast and drop spreaders operate using gravity. Gravity causes the fertilizer granules to drop from the hopper.
The setting controls how fast the fertilizer granules drop from the hopper.
Fertilizer granules drop at the same speed, regardless of whether the applicator is running or standing still.

## Slide 41: Equipment Calibration
Changing walking speed changes the fertilizer application rate.
The applicator must maintain the same speed all day, every day.
Practice walking using a watch with a second hand, a metronome or a song with a steady beat.

## Slide 42: Field Adjustments
Check the total amount of fertilizer applied after half a day. Does the amount applied match what should have been applied based on property size?
If not, and your walking speed has not changed, you may need to adjust the setting up or down slightly.
The CPFA should provide guidance for field adjustments.

## Slide 43: Field Adjustments cont’d
As equipment wears, the setting may need to be adjusted.
Changes may be temporary. High humidity can cause fertilizer pellets to stick together.
If you have adjusted the setting to compensate for humidity, remember to change back the next day.

## Slide 44: Spreader Calibration
Spreaders should be calibrated at least annually and whenever something changes, for example, changing from lime to fertilizer.
If equipment or parts are changed, the spreader should be re-calibrated.

## Slide 45: Spreader Calibration cont’d
The CPFA will determine the swath width and instruct you on how far apart each successive pass should be.

## Slide 46: Hose & Gun Sprayer Calibration
The CPFA is responsible for selecting the correct nozzle and calibrating the hose & gun sprayer.
As with a drop spreader or a broadcast spreader, pace is critical. The trained applicator should practice pace on a training course set up by the CPFA

## Slide 47: Hose & Gun Sprayer Calibration cont’d
Check the flow rate each day to make sure it has not changed.
If your supervisor does not perform this task, he or she should instruct you how to perform a bucket check following the procedures in the Maryland Professional Lawn Care Manual.

## Slide 48: Check your equipment
Inspect your equipment daily to ensure that it continues to operate properly.
Clean equipment as needed to prevent blocked openings and ensure the impeller spins freely.

## Slide 49: Reading a Fertilizer Label

## Slide 50: How to read a fertilizer label
Looking at a bag of fertilizer, you will see 3 numbers, for example: 22-0-10
These three numbers tell you the percent by weight of the 3 most important fertilizer ingredients:
% Total Nitrogen (N), % Available Phosphate (P2O5), and soluble Potash (K2O)
Note that by convention in the fertilizer industry, the numbers do not indicate elemental phosphorus (P) or potassium (K).

## Slide 51: 22-0-10
The numbers on the fertilizer bag are always listed in the same order: N-P2O5-K2O
This fertilizer contains 22% nitrogen and 10% potash (K2O), but no phosphate (P2O5)
To determine how much of a nutrient is contained in a bag of fertilizer, multiply the weight of the bag by the percent of the nutrient, expressed as a decimal.
A 50 lb bag of 22-0-10 would contain (50 X 0.22) or 11 lbs of N, and (50 X 0.10) or 5 lbs of K2O.

## Slide 52: Some Bags Have 4 Numbers
  10-0-7-2
The 4th number can be anything except nitrogen, phosphorus, or potassium.
Read the label to find out what it is.

## Slide 53: Forms of Nitrogen
  There are 2 main forms of nitrogen that may be contained in the fertilizer.
  Quick release or water soluble nitrogen (WSN)
  Slow release, controlled-release, or water insoluble nitrogen (WIN)
  The law limits how much soluble nitrogen and how much total nitrogen may be applied

## Slide 54: Forms of Nitrogen cont’d
Quick release nitrogen is immediately available for uptake by the grass. It is also more likely to leach into the groundwater.
Slow release nitrogen provides a continuous supply of nitrogen to the grass over an extended period of time. It won’t, however, cause the grass to immediately green up.
The ideal turf fertilizer contains a combination of quick release and slow release nitrogen.

## Slide 55: Provisions of the Lawn Fertilizer Law

## Slide 56: Nitrogen Limits
A single fertilizer application may contain no more than 0.7 lb/1000 sq ft of soluble nitrogen and no more than 0.9 lb/1000 of total nitrogen.
The annual amount of nitrogen applied is limited to the amount recommended by the University of Maryland Extension, and depends on the type of grass being fertilized and the use of the area.

## Slide 57: Phosphorus Limits
Fertilizer applied to turf may not contain phosphorus unless:
A soil test, that is not more than 3 years old, indicates there is a need; or
Turf is being established or re-established and the ground has been tilled, or otherwise disturbed, such as with construction; or
A lawn patch product is used (seed, fertilizer, and mulch combination).

## Slide 58: The Certified Professional Fertilizer Applicator is responsible for selecting the appropriate fertilizer and determining the application rate.

## Slide 59: Stay away from water!
Nitrogen and phosphorus cannot be applied to turf within 15 feet of water.
If the application is made with a drop spreader, a broadcast spreader with a deflector shield, or a targeted spray, the buffer can be reduced to 10 feet.

## Slide 60: This is water, too!

## Slide 61: Do not apply before or during a heavy rain, or when the ground is frozen. Do not apply to impervious surfaces. Fertilizer that lands on impervious surfaces must be swept or blown back onto the turf.

## Slide 62: Timing
Do not apply nitrogen or phosphorus to turf before March 1st or after December 1st.
From November 16 until December 1st, no more than 0.5 lbs of soluble or insoluble nitrogen may be applied per 1000 square feet.

## Slide 63: Questions?
Call or e-mail the Maryland Department of Agriculture, Nutrient Management Program
410.841.5959
800.492.5590 toll free
Nminfo.mda@maryland.gov